## Slide 1
CSE-3213
Computer Graphics Lecture 20

## Slide 2: Video Display Devices
Cathode-ray tube (CRT) Monitor
Rater-Scan Displays
Random-Scan Displays
Color CRT Monitors
Flat-Panel Displays

## Slide 3: Cathode-ray tube (CRT) Monitors
The primary output device in a graphics system is a video monitor.
The operation of most video monitors is based on the standard cathode-ray
tube (CRT) design

## Slide 4: Cathode-ray tube (CRT) Monitors

## Slide 5: CRT

## Slide 6: CRT types
Raster-scan (point by point refreshing)‏
Refresh rate: # of complete images (frames) drawn on the screen in 1 second. Frames/sec.
Frame time: reciprocal of the refresh rate, time between each complete scan. sec/frame

## Slide 7: Cathode-ray tube (CRT) Monitors
Refresh CRT
Beam of electrons hit phosphor-coated screen, light emitted by phosphor
Direct electron beam to the same screen repeatedly, keeping phosphor activated
The frequency at which a picture is redrawn on the screen is referred to as the “refresh rate”
The maximum number of points that can be displayed on a CRT is referred to as the “resolution”
Display principle
Raster Scan Display Principle
Random Scan Display Principle

## Slide 8: CRT Display Principles
Raster-Scan Displays
  Based on TV technology
    Electron beam swept across screen one row at a time from top to bottom
    Each row is referred to as a scan line

## Slide 9: CRT Display Principles
© 2005 Pearson Education
Raster-Scan Displays
  Picture elements: screen point referred as “Pixel”
  Picture information stored in refresh (frame) buffer

## Slide 10: CRT Display Principles
Raster-Scan Displays
  Picture information stored in refresh (frame) buffer
    The number of bits per pixel in the frame buffer is called depth or bit planes
    Buffer with 1 bit per pixel – Bitmap
    Buffer with multiple bits per pixel – Pixmap
  Interlaced refresh procedure
    Beams sweeps across every other scan line

## Slide 11: Frame Buffer
A frame buffer is characterized by size, x, y, and pixel depth.
the resolution of a frame buffer is the number of pixels in the display. e.g. 1024x1024 pixels.
Bit Planes or Bit Depth is the number of bits corresponding to each pixel. This determines the color resolution of the buffer.
Bilevel or monochrome displays have 1 bit/pixel
8 bits/pixel -> 256 simultaneous colors
24 bits/pixel -> 16 million simultaneous colors

## Slide 12: Specifying Color
direct color :
  each pixel directly specifies a color value
    e.g., 24bit : 8bits(R) + 8bits(G) + 8 bits(B)
Green
Red
Blue
8
8
8

## Slide 13: Refresh Rates and Bandwidth
Frames per second (FPS)

## Slide 14: Interlaced Scanning
Interlacing of the scan lines in this way allows us to see the entire screen displayed in half the time that it would have taken to sweep across all the lines at once from top to bottom.
To reduce flicker, divide frame into two fields—one consisting of the even scan lines and the other of the odd scan lines.
Even and odd fields are scanned out alternately to produce an interlaced image.

## Slide 16: Aspect Ratio
which is now often defined as the number of pixel columns divided by the number of scan lines that can be displayed by the system. (Sometimes this term is used to refer to the number of scan lines divided by the number of pixel columns.)
Aspect ratio can also be described as the number of horizontal points to vertical points (or vice versa) necessary to produce equal-length lines in both directions on the screen.
Frame aspect ratio (FAR) = horizontal/vertical size
    TV 4:3
    HDTV 16:9

## Slide 18: CRT Display Principles
Random-Scan Display Principles
  Electron beam directed only to the points of picture to be displayed.
  Vector displays, electron beams trace out lines to generate pictures
  Picture stores as a set of line-drawing commands
    Storage referred as display list, refresh display file, vector file or display program

## Slide 19: CRT Display Principles
Sample of Random-Scan displays principles

## Slide 20
Thank you